## Slide 2
Notes: 1. Late summer, at home, watch them grow, pears, apples, berries
2. Pored in love, time, effort
1. One morning…

## Slide 3
Notes: 1. It was all gone…
2. The culprit. Deer
3. This is my revenge story.

## Slide 4
SENTRY

## Slide 5
SENTRY

## Slide 6
+ + + + +
+ + + + +
+ + + +
SENTRY
Notes: Not the only person

## Slide 7: Our Team
Mark Gladkevitch
Amaziah Kinavuidi
Notes: Before we get into the project details, we’ll briefly introduce our team. I’m Amaziah, the lead software engineer who trained the AI computer-vision model and programmed the device.

## Slide 9: Agenda
Project overview
Hardware
  PCB
  Parts used and deterrents
Software
  Tracking model
  Motor control
Final Remarks
Project Overview
Notes: Now, this is what we will table about today. We’ll go over what our project is and what it does, then then dive deep into the hardware and software aspect of our project. And at the end, we’ll make a few closing remarks.

## Slide 10: Project Overview
Notes: An ai computer vision model …………

## Slide 11: Project Overview
DETECT
DETER
Notes: So, our Sentry Project It can be summed up in two words: detect and deter — which is our two main goals. If you remember only one thing today, let it be that.

## Slide 12
What is the sentry turret and what does it do?
The sentry turret is an autonomous system that uses an AI model to detect, track and deter deer using a laser.
DETECT
DETER
Project Overview
Notes: So How does it work? It’s an autonomous AI-powered system that detects, tracks, and deters deer with a laser. From the start, we focused on making it fast, accurate, and reliable—something people can use to protect their property and plants.

## Slide 13: Hardware
Sensing
Brains
Power
Movement

## Slide 14: Hardware
Sensing
Brains
Power
Movement

## Slide 15: Hardware
100-degree field of view (FOV)
USB type A connector
Capable of 30 frames per second (fps) at 1280x720 pixel resolution
Night vision capable with IR CUT filter
Sets turning distance boundaries
Sets homepoint
Powerful/Fast chipset (2.4Ghz)
Easy to operate and program
Wide array of available connections
Plenty of experience
Great for controling motors, sensors, deterrents
Available in electronics prep room
Can handle high currents (over 1.5A)
Raspberry Pi
Arduino
Motor Control Module
Sensing
Brains
Power
Motion
Notes: Stress how it aligns with our goal to make it precise and accurate

## Slide 16
100-degree field of view (FOV)
USB type A connector
Capable of 30 frames per second (fps) at 1280x720 pixel resolution
Night vision capable with IR CUT filter
Sets turning distance boundaries
Sets homepoint
Powerful/Fast chipset (2.4Ghz)
Easy to operate and program
Wide array of available connections
Plenty of experience
Great for controlling motors, sensors, deterrents
Available in electronics prep room
Can handle high currents (up to 2A)
Raspberry Pi
Arduino
Motor Control Module
High speed (1200rpm)
Precise
Cheap(er)
Sacrificing speed for higher torque
Can turn more weight
NEMA 17 Stepper Motor
10:1 Gears
Sensing
Brains
Power
Motion

## Slide 17
Sensing
Brains
Power
Motion
High speed (1200rpm)
Precise
Cheap(er)
Sacrificing speed for higher torque
Can turn more weight
NEMA 17 Stepper Motor
10:1 Gears
Has many different available voltages (3.3V, 5V, 12V)
High current availability
Free

## Slide 18
Sensing
Brains
Power
Motion
High speed (1200rpm)
Precise
Cheap(er)
Sacrificing speed for higher torque
Can turn more weight
NEMA 17 Stepper Motor
10:1 Gears
Has many different available voltages (3.3V, 5V, 12V)
High current availability
Free
ATX Power Supply

## Slide 19
Sensing
Brains
Power
Motion
High speed (1200rpm)
Precise
Cheap(er)
Sacrificing speed for higher torque
Can turn more weight
NEMA 17 Stepper Motor
10:1 Gears
Has many different available voltages (3.3V, 5V, 12V)
High current availability
Free
All power cords from devices merged into one wall outlet cord
Arduino mount + extra free I/O pins
Extra USB type A
Mounted Arduino Uno
PSU connector
Extra I/O pins
Screw terminals

## Slide 20
Deterrents
5mW Green Laser
Aiming for sub 10 Minute Of Angle (MOA)
1 MOA = deviation of 1 inch per 100 yards
(For proof of concept)

## Slide 22: Software

## Slide 23: Software
Computer vision
Deterrents control
Programmed in python
Capture frames from the USB cam and run inference on it
Programmed in C using the Arduino IDE
Control the movement of the laser and its activation

## Slide 24: Software
Computer vision
Deterrents control
Programmed in python
Capture frames from the USB cam and run inference on it
Programmed in C using the Arduino IDE
Control the movement of the laser and its activation
Using an Ultralytics YOLO AI model
Ultralytics is a software company that develops and provides open-source models
Computer vision - YOLO AI model
Notes: Our software is made up of 2 different parts, computer vision on the pi 5 which is programmed in python. That handles the capturing of frames from our usb cam and running inference on it to check for detections. If there’s a detection, it grabs the coordinates of the deer within that frame and sends it to the Arduino uno. The Arduino microcontroller is programmed in c using the Arduino software. It receives the coordinates from the pi 5 then does some conversions to move the motors.

## Slide 25: Computer vision - YOLO AI model
Using an Ultralytics YOLO AI model
Ultralytics is a software company that develops and provides open-source models
Notes: Now let’s dive deeper into the computer vision section. So, we’re using YOLO AI model by ultralytics. Ultralytics is basically a computer vision AI company that develops and provides open-source solutions models.

## Slide 26: Computer vision – YOLO AI model cont.
Computer vision – Training a model
Deer dataset of 1211 images from Roboflow
Add preprocessing and augmentation layers to have a diverse set of images
Trained models with 70 -100 epochs
Notes: From all of those available models. We chose the nano version of the yolov8 model because it was one of the fastest models that runs well within the pi 5 capabilities. It is fast and provides accurate results as well.

## Slide 27: Computer vision – YOLO AI model cont.
Computer vision – Training a model
Deer dataset of 1211 images from Roboflow
Add preprocessing and augmentation layers to have a diverse set of images
Trained models with 70 -100 epochs
For every detected deer, a bounding box is drawn around the deer
Display confidence level and tracking number
Computer vision – Test
Notes: So we got our deer dataset containing 1200 images of a deer from roboflow universe. We added different preprocessing and augementation layers such as britness, auto orient, noise and some other ones, to make our model robust. We dataset to have a variety of images of deer in different environments, lightning conditions and in different positions too. After getting the images in ready, we trained the YOLO model on it with 70-100 epochs, which is basically the number of passes the model goes through the images.

## Slide 28: Computer vision – Test
Computer vision – Training a model
Deer dataset of 1211 images from Roboflow
Add preprocessing and augmentation layers to have a diverse set of images
Trained models with 70 -100 epochs
For every detected deer, a bounding box is drawn around the deer
Display confidence level and tracking number
Computer vision – Wrap-Up
Model successfully trained
Detects new data accurately
Extract the raw coordinates of a deer within a frame with a center point then send it to the Arduino through serial communication
Notes: Next up, we use that model we’ve trained. The way it works is it basically draws a bounding box around a detected deer, give it an id number for tracking, finds the center point then displays a confidence level, which is a number out of 1, that shows how confident the model is on the detected object. extracts those coordinates

## Slide 29
Computer vision – Training a model
Deer dataset of 1211 images from Roboflow
Add preprocessing and augmentation layers to have a diverse set of images
Trained models with 70 -100 epochs
Computer vision – Wrap-Up
Model successfully trained
Detects new data accurately
Extract the raw coordinates of a deer within a frame with a center point then send it to the Arduino through serial communication
Motor control for deterrents – Arduino Uno
Receive raw coordinates from the Raspberry pi 5
Do conversions and map pixel coordinates to actual motors steps
Turn on the laser and move the motors to deer location
Notes: So we successfully trained our trained our model, although there was a lot of trial. Our model can detect new data and get the coordinates from a detected deer.

## Slide 30
Computer vision – Wrap-Up
Model successfully trained
Detects new data accurately
Extract the raw coordinates of a deer within a frame with a center point then send it to the Arduino through serial communication
Motor control for deterrents – Arduino Uno
Receive raw coordinates from the Raspberry pi 5
Do conversions and map pixel coordinates to actual motors steps
Turn on the laser and move the motors to deer location

## Slide 31: Motor control for deterrents – Arduino Uno
Computer vision – Wrap-Up
Model successfully trained
Detects new data accurately
Extract the raw coordinates of a deer within a frame with a center point then send it to the Arduino through serial communication
Receive raw coordinates from the Raspberry pi 5
Do conversions and map pixel coordinates to actual motors steps
Turn on the laser and move the motors to deer location
Notes: Deterants activation

## Slide 32: Finance
Had a budget of $ 500
We have spent $ 195 on parts
Managed to stay under our budget

## Slide 33: Finance
Had a budget of $ 500
We have spent $ 195 on parts
Managed to stay under our budget

## Slide 34
Final Remarks
Notes: Slide about how training it on deer is hard due to lack of data and support.
We were just asked by the college to not track people. Training it on humans is much easier, faster, and more precise. - emphasise its wide usage for trained models on people like paintball arenas, home defence, military.
Stress how much cheaper this would be compared to a high-tech military turret if used for military
Garnered interest from Kommando Hubschrauber regiment
And Ukrainians

## Slide 35
(Blown up PLC)
Notes: 1. Our journey – difficult - understatement
2. Brick walls
3. Each endured their own version
4. Worries, struggles, question why u here,
yet you chose to keep going
5. Desperate deadlines, comrades fall one by one
6. Not many made through
Every inch!!!!!
7. Every lab…………. Shaped ppl
8.Our hard work, testament
And truth is……
9. Not everyone made it here
Earned place, earned moment
Thank you
God bless

## Slide 36
+ + + + +
+ + + + +
Your property’s safety is our priority